CESSNA P 337 H

Pressurized

Skymaster

N777SN

Quick reference training guide

This training manual cannot be used as a substitute for the official pilots operating handbook.

1. Take off  (normal)

Normal flaps for short runway  1/3

Lead with rear engine

37" 2800 RPM (mind over boost) (33"for training)

Vr: 						75 KIAS

Flaps up 					80 KIAS

Gear up 					89 KIAS

Cruise Climb					115 KIAS 31” 2450 RPM

Fuel flow  					90/90 lbs green/green

2. Take off  (short runway)

Flaps 						1/3 Brakes hold

Power 						37" 2800 RPM

Fuel flow 					90/90 lbs/hr green/green

Brakes 						release

Attitude						Low tail

Vr 						70 KIAS

VCs 						80 KIAS (obstacles)

Flaps up 					(80 KIAS)

Vy 						Gear up (89 KIAS)

Cruise Climb					115 KIAS 31“ 33" 2450RPM

3.	Max. Performance Climb

Attitude						B A + 12 degrees

Speed 						95 KIAS

Power						2600 RPM/37"

Fuel flow 					90/90lbs/hr green/green

Cowl flaps 					open

4. Normal Cruise Climb

Attitude					B A +7 degrees

Speed 						120 KIAS

Power						31" 2450 RPM (SL. up to 15000)

Fuel flow 					90 /90 lbs/hr green/green

Cowl flaps  					as required

5. Cruise (65%)

Power						2400 RPM 29" up to 14.000 ft

Mixture 					70/70 lbs peak EGT -/-50 F

Cross feed at level flight  - 		Stop AT 50 LBS - Full or empty 								tanks (either)

NOTE

15.000 ft - 18.000 ft					2500/29"

19.000 ft -  20.000 ft				2600/27"

Add 1" for ISA + 10

6. Descent

Cabin pressure -			> set  + 500 feet

Power					25"/2400 RPM  (min 20")

Mixture 				Adjust

Anti Ice				as required

7. Normal Visual Circuit

DOWNWIND

Speed					140 KIAS

Power					25" / 2400 RPM

Approach checklist 			completed

ABEAM-Landing Threshold

Timing				3 sec/100 ft

Flaps					1/3

Gear					down

Speed					110 KIAS

Power					25" / 2400 RPM

BASE LEG

Power					20" / 2400 RPM

Flaps					2/3

Speed					100 KIAS

Before landing checklist		completed

FINAL

Power					17"/2400 RPM

Speed					90 KIAS

Flaps					Full

SHORT FINAL (VTgT Headwind component 10 KTS or less)

Speed					85 KIAS

Power					as required

Propeller levers			max. RPM (below 15")

Mixture 				Fully rich

8. Short Field Landing

Fly normal pattern

Final					Steeper angle

Flaps					Full

Power					as required / max. RPM (fully fine)

Speed					78 KIAS

9. Flapless

DOWNWIND

Speed					140 KIAS

Power					25" / 2400 RPM

ABEAM LANDING THRESHOLD

Timing				3 sec./100ft

Gear					Down

Speed					135 KIAS

Power					25" / 2400 RPM

BASE LEG

Power					17"/2400 RPM

Speed					105 KIAS

Before landing checklist 		completed

FINAL

Speed					90 KIAS

Power					2400 RPM /as required

Short Final				MAX. RPM (below 15")

10. GO AROUND

Power					37" / 2800 RPM (33" for training)

Flaps					Retract to 1/3

Speed					80 KIAS

Above obstacles			Flaps up

Speed 89 KIAS			Gear up

Cowl flaps				Open

Note: Do not retract gear if another approach is to be conducted.

11. Go - no go decision - one engine out

NO GO

Airspeed below			80 KIAS

Below obstacles			(no possibility for circumnavigation)

Runway available			Land

GO

Airspeed				> 80 KIAS

No runway				Available

Above obstacles			above obstacles or possible for circum 							navigation

ENGINE FAILURE AFTER TAKE-OFF ACTIONS

Throttles, Props, Mixtures		Full forward

Inoperative engine			Identify

Inoperative engine			Throttle closed

Inoperative engine			Feather

Inoperative engine			Cowl flaps close

Airspeed 80 KIAS			Flaps up

Above obstacles			Accelerate 89 KIAS

89 KIAS (bleu line)			Retract gear

ATC					Call

Inoperative Engine securing Checklist

Check					Box items

Mixture				Idle cut off

Alternator				Off

Ignition Switch			Off

Fuel selector				Off (red)

Synchrophaser			Off

Electrical Load			Reduce

Inop. Engine				Attempt restart

ZERO TRUST 			12 MAP

12. Engine failure above 1000ft AGL and in cruise

Throttles, Props, Mixtures		full forward (slowly)

Inoperative engine			identify

Mixture inoperative engine	RICH

Aux. Fuel Pump (inop. engine)	On HIGH

Fuel selector (inop. engine)	cross feed

Check immediately	Restart	On fuel flow

IF NOT

Aux. Fuel Pump			OFF

Inoperative Engine			Feather /secure

Live Engine				Power as required

13. Engine restart in flight.

(Feathered and equipped with unfeather accumulators)

Fuel selector 			Green on proper tank

Throttle 				Just out of gear warning

Propeller				Cruise rpm position

UN feathering				Check

Aux. fuel pump 			High

Ignition				Both or start if no unfeathering

Mixture				Adjust for fuel flow 10-35 lbs

Aux. fuel pump 			off

Oil pressure				Checked

Alternator				On and checked

Power	 (200 degrees F.)		Reset

14. One engine inoperative Visual approach and landing

DOWNWIND

Speed					110 KIAS

Power					33 / max. RPM

Fuel selector operating engine	Green

Approach checklist			completed

BASE LEG

On profile				gear down

Speed					110 KIAS

Power					30" / max. RPM

Before landing checklist		completed

FINAL

Flaps					1/3

Speed					110 KIAS

Power					Max. RPM

LANDING ASSURED

Flaps					as required

Speed 				90 KIAS

Threshold				85 KIAS

15. Two Engine Instrument Approach

OUTBOUND

Flaps					1/3

Gear					Down

Speed					120 KIAS

Power					25" 2450 RPM

ON GLIDE (within 10 degrees)

Flaps					2/3

Speed					110 KIAS

Power					20" / 2450 RPM

VISUAL

Flaps					As required

Speed					90 KIAS

Speed on short final			85 KIAS

16. One engine inoperative instrument approach

OUTBOUND

Speed					110 KIAS

Power					33" / Max. RPM

Fuel selector Operating Engine	Green

ON GLIDE

Gear					Down

Flaps					1/3

Speed					110 KIAS

Power					30" MAX. RPM

LANDING ASSURED

Flaps					As required

Speed					90 KIAS

Threshold					85 KIAS

Note

Non-precision Approach: No flaps until visual and on glide!

17. Air work

STEEP TURNS 45 degrees

1.	PREPARATION

Speed 140 KIAS (2400/ 25")

Set heading bug

2.	EXECUTION

The exercise consists of two 360 deg. turns to the one direction and immediately followed by two 360 deg. turns opposite.

Anticipate heading on roll out +/- 10 deg.

Add +/- 2" after 30 deg. bank and reduce again on roll out.

STALLS (pressurization off)

1.	PREPARATION

Speed 140 KIAS (2400/ 25")

Altitude +2500 ft AGL

Area not over populated zones

Clearing turns for look out

2.	STALL CLEAN

Level flight, set heading bug

Power smoothly idle

Keep level flight

Trim speed 90 KIAS

Recovery: 	Power 33"

Attitude 0 deg.

At 90 KIAS rotate  +10 deg.

Reduce power 31"

3.	STALL GEAR DOWN FLAPS 2/3 30 deg. BANK

Level flight set heading bug

Flaps 1/3 gear down 110 KIAS

Power 2400/20" flaps 2/3

Bank 30 deg

Trim speed 80 KIAS

Recovery: 	Power 33"

Attitude -5 deg. BA

At 80 KIAS wings level

Flaps 1/3

Rotate + 10 deg.

Positive climb flaps up

89 KIAS gear up

Reduce power 31"

4.	STALL IN LANDING CONFIGURATION

Level flight, set heading bug

Flaps 1/3 gear down 110 KIAS

Power 20"/2400

Flaps 2/3 100 KIAS

Power 17" /2400

Flaps full

Trim speed 80 KIAS

Recovery: 	Power 33"

Attitude -5 deg. BA

Flaps 1/3

At 80 rotate + 10 deg.

Positive climb flaps up

89 KIAS gear up

Reduce power 31"

Informatie bijgewerkt tot  31 mei 2000